## Slide 1: Electromagnetics
Farhad Mazlumi
Assistant Professor
Civil Aviation Technology College, Tehran

## Slide 2: Introduction

## Slide 3: Development of scientific subject
Approaches in the development of scientific subject
  Inductive approach: starts with the observation of some experiments and infers from them laws and theorems.
  Deductive approach: postulates a few fundamental relations for an idealized model from which particular laws and theorems can be derived.
We use the deductive approach.

## Slide 4: Modeling
Three steps to build an idealized model:
  Define basic quantities
  Specify the rules of operations (the mathematics)
  Postulate fundamental relations

## Slide 5: Example: Circuit theory
  Quantities: voltage (V), current (I), resistance (R), capacitance (C), inductance (L).
  Rules of operations: algebra, ordinary differential equations, and Laplace transformation
  Postulates: Kirchhoff's voltage and current laws (KVL and KCL)

## Slide 6: Electromagnetic Model
  Quantities: basic quantities of electromagnetics (chapter 1)
  Rules of operations: vector algebra, vector calculus, and partial differential equations (chapter 2)
  Postulates: Maxwell’s equations
    Electrostatics (chapter 3)
    Magnetostatics (chapter 6)
    Faraday’s law and displacement current (chapter 7)

## Slide 7: Quantities in Electromagnetics Model
Source quantities
  Electric charge
  Electric current
Field quantities

## Slide 8: Source Quantities: Electric Charge
  Electric charge (Q or q): unit of charge is C (Coulomb).
    Two kinds of charges: positive and negative.
    Microscopic sense: discrete (e  1.6010-19C)
    Macroscopic sense: continuous
    Point charge
    Charge distributions
Volume charge density (C/m3) Surface charge density (C/m2) Line charge density (C/m)

## Slide 9: Source Quantities: Electric Current
  Electric current (I or i): unit of electric current is A (Ampere).
    Electric current is a flow of electric charge.
    Electric current flows through a finite area or cross section.
    Electric current (A), Volume current density (A/m2), Surface current density (A/m)

## Slide 10: Quantities in Electromagnetics Model (cont.)
Field quantities
Quantity | Symbol | Unit
Electric field intensity | E | V/m
Electric flux density | D | C/m2
Magnetic flux density | B | T, Wb/m2
Magnetic field intensity | H | A/m

## Slide 11: Postulates in Electromagnetics Model
Principle of conservation of electric charge
Constitutive relations
Maxwell equations

## Slide 12: Principle of conservation of electric charge
Conservation of charge is the principle that the total electric charge in an isolated system never changes. The net quantity of electric charge, the amount of positive charge minus the amount of negative charge in the universe, is always conserved.
Continuity equation

## Slide 13: Postulates in Electromagnetics Model
Constitutive relations of a medium
  Medium electrical parameters
    Electric permittivity  (F/m)
    Magnetic permeability  (H/m)
    Electric conductivity  (S/m)
Universal constant | Symbol | Value | Unit
Velocity of light in free space | c |  299792458 | m/s
Permeability in free space | 0 | = 410-7 | H/m
Permittivity in free space | 0 |  8.85410-12 | F/m

## Slide 14: Ampere Definition in SI (until 2019)
The ampere is that constant current which, if maintained in two straight parallel conductors of infinite length, of negligible circular cross-section, and placed one meter apart in vacuum, would produce between these conductors a force equal to 210−7 newtons per meter of length.

## Slide 15: Maxwell Equations
Differential form in time domain