## Slide 1: Electromagnetics
Farhad Mazlumi
Assistant Professor
Civil Aviation Technology College, Tehran

## Slide 2: Vector Calculus

## Slide 3: Quantity
A physical quantity (or simply quantity) is a property of a material or system that can be quantified by measurement.
A physical quantity can be expressed as a value, which is the algebraic multiplication of a numerical value and a unit of measurement.
Quantities in electromagnetics can be functions of time and position.

## Slide 4: Field
A field is a spatial distribution of a quantity, which may or may not be a function of time.

## Slide 5: Categories of Quantities
Scalar
  At a given time and position, a scalar is completely specified by its magnitude (positive or negative, together with its unit).
  Example: electric charge
Vector
  At a given time and position, a vector requires both a magnitude and a direction.
  Example: Electric field intensity
E

## Slide 6: Tensor
A tensor is a mathematical object that provides a coordinate-independent description of a physical property.
It is a Geometric Object:
  This means a tensor represents a well-defined entity that exists in space, independent of how we choose to describe it. Think of it as a physical “thing” (like electric field intensity, or the permittivity of an anisotropic medium) rather than a mere list of numbers.
It is Coordinate-Independent:
  The physical reality the tensor represents does not change when we change our coordinate system (e.g., rotating our x, y, z axes). However, its components—the specific set of numbers we write in a matrix to represent it—do change in a very precise and compensatory way.

## Slide 7: Tensor Ranks
The rank of a tensor indicates the number of indices needed to describe it in a given coordinate system. It classifies physical quantities by their geometric complexity.
Rank | Common Name | Example in Electromagnetics | Description
0 | Scalar | Electric charge (Q), Potential (V), Energy (W) | A single, coordinate-independent number.
1 | Vector | Electric field intensity (E), Magnetic flux density (B), Current density (J) | Describes magnitude and direction. Requires 3 components (in 3D) that transform together under rotation.
2 | Tensor (Dyadic) | Permittivity tensor (ϵij​), Permeability tensor (μij​) | Relates two vectors. Requires 9 components (in 3D) that transform in a specific way. Describes anisotropy or complex relationships.

## Slide 8: Vector vs. Set of Three Numbers
A set of three numbers is a vector (rank-1 tensor) only if the numbers represent components along directions in a geometric space that transform together under coordinate changes.
(3 apples, 2 oranges, 5 peaches) is not a vector. This is just a tuple of scalars. Each item (apple count, orange count, peach count) is a scalar: a coordinate-independent number.
(Ex​ = 3 V/m, Ey​ = 2 V/m, Ez​ = 5 V/m) is a vector. The components of a vector are not independent numbers; they mix (transform) in a specific way under coordinate rotation, as seen with electric field components.

## Slide 9: Magnitude and Unit Vector
A
|A|
A
Magnitude of vector A: |A| or A
Unit vector of A:
Note: A has the unit and dimension of A.
Note: unit vector is dimensionless.

## Slide 10: Vector Addition and Subtraction
A
B
A
B
A+B
A
-B
A-B
A+B
A-B = A+(-B)

## Slide 11: Products of a Vector and a Scalar
Multiplication of a vector (A) by a positive scalar (a > 0)
Multiplication of a vector (A) by a negative scalar (a < 0)
A
aA
A
aA

## Slide 12: Dot Product
Applications:
  Magnitude of a vector
  Vector projection
B
A

B
A

b

## Slide 13: Properties of Dot Product
Commutative law
Distributive law

## Slide 14: Cross Product
Applications:
  Area of parallelogram
  Normal vector
B
A

B
A
B
A

S

## Slide 15: Properties of Cross Product
NOT commutative
Distributive law
NOT associative

## Slide 16: Properties of Three Vectors
B
C
A
Volume of the parallelepiped formed by the three vectors A, B, and C

## Slide 17: Orthogonal Coordinate Systems
Mathematical representation of
  the location of a point
  a vector
A
P
Point
Vector

## Slide 18: Coordinates of a point
Three-dimensional space  (u1, u2, u3)
u1 = 10
u1 = 10
u2 = 12
u1 = 10
u2 = 12
u3 = 15

## Slide 19: Base Vectors
Unit vectors
u1 = 10
u2 = 12
u3 = 15
u2 = 12
u3 = 15

## Slide 20: Base Vectors
Right-handed Orthogonal Coordinate System

## Slide 21: Vector Representation
A

## Slide 22: Addition, Subtraction, and Products

## Slide 23: Dot Product of Two Vectors
B
A
C

1 Vector Subtraction
2 Law of Cosines
1
2

## Slide 24: Differential Length
Some of the coordinates may not be a length.
Metric coefficients: h1, h2 and h3
dl
C

## Slide 25: Differential Area
u1 = 10

## Slide 26: Differential Volume

## Slide 27: Orthogonal Coordinates Systems
Cartesian coordinates
Cylindrical polar coordinates
Spherical coordinates
Parabolic coordinates
Paraboloidal coordinates
Ellipsoidal coordinates
Bipolar cylindrical coordinates
Reference: https://en.wikipedia.org/wiki/Orthogonal_coordinates

## Slide 28: Cartesian Coordinate System
(u1, u2, u3) = (x, y, z)
h1 = 1, h2 = 1, h3 = 1

## Slide 29: Cylindrical Coordinate System
(u1, u2, u3) = (r, , z)
r  0
0   < 2

## Slide 30: Cylindrical Coordinate System
h1 = 1, h2 = r, h3 = 1

## Slide 31: Spherical Coordinate System
(u1, u2, u3) = (R, , )
0   < 2
0    

## Slide 32: Spherical Coordinate System
h1 = 1, h2 = R, h3 = Rsin = r

## Slide 33: Exercise: Sum of Two Vectors
33

## Slide 34: Exercise: Dot Product of Two Vectors
34

## Slide 35: Unit Vectors on z-axis
35

## Slide 36: Position Vector
R
R
R
A position vector is a vector that represents the location of a point in space relative to a fixed origin, typically expressed in terms of its coordinates.

## Slide 37: From Cylindrical to Cartesian Coordinates
Point coordinates

## Slide 38: From Cartesian to Cylindrical Coordinates
Point coordinates
?

## Slide 39: From Cylindrical to Cartesian Coordinates
Vector expression

## Slide 40: From Cylindrical to Cartesian Coordinates (cont.)
Vector expression

## Slide 41: From Cartesian to Cylindrical Coordinates
Vector expression

## Slide 42: From Spherical to Cartesian Coordinates
Point coordinates

## Slide 43: From Cartesian to Spherical Coordinates
Point coordinates
?

## Slide 44: From Spherical to Cartesian Coordinates
Vector expression

## Slide 45: From Spherical to Cartesian Coordinates (cont.)
Vector expression

## Slide 46: From Cartesian to Spherical Coordinates
Vector expression

## Slide 47: Integrals Containing Vector Functions
Volume Integral of a Vector Function
Line Integral (Path Integral) of a Vector Function
Surface Integral of a Vector Function

## Slide 48: Vector Function
Vector function (or vector field): a spatial distribution of a vector quantity

## Slide 49: Vector Function (examples)

## Slide 50: Volume Integral of a Vector Function

## Slide 51: Parametric Representation of Paths
Path: a one-dimensional curve in space.
It can be mathematically described using a single independent parameter (usually denoted as t).
x
y
z
t1
t2
t
R(t)
C

## Slide 52: Differential Path Element
O
t
R(t)
R
t+t
R(t+t)

## Slide 53: Differential Path Element (cont.)

## Slide 54: Differential Path Element (cont.)
F(t)
dl(t)
t
C
t1
t2

## Slide 55: Line Integral of a Vector Function

## Slide 56: Line Integral of a Vector Function (example)

## Slide 57: Line Integral of a Vector Function (example)

## Slide 58: Parametric Representation of Surfaces
Surface: a two-dimensional object in space.
It needs two independent parameters (usually denoted as u and v).
x
y
z
R(u,v)
S
(u,v)

## Slide 59: Differential Surface Element
S
(u,v)
(u+u,v)
(u,v+v)
O
s
R

## Slide 60: Surface Integral of a Vector Function
S
(u,v)
O
ds
R
F

## Slide 61: Parametric Representation of Surfaces (example)
Notes: Plot the surface

## Slide 62: Parametric Representation of Surfaces (exercise)
z
y
x
z
y
x
0

## Slide 63: Vector Differential Operators
Three primary operations that are essential for describing electromagnetic fields:
  Gradient
  Divergence
  Curl
Each one has a distinct physical interpretation.
These operators are defined using the del symbol ().

## Slide 64: Gradient of a Scalar Field
Input: a scalar field, e.g. f(R) Output: a vector field, e.g. F(R)
Scalar field
Vector field
Gradient symbol

## Slide 65: Gradient of a Scalar Field (cont.)
Gradient magnitude: Rate of maximum increase
Gradient direction: Steepest ascent
Scalar field
Vector field
Gradient symbol
Gradient direction
Gradient magnitude

## Slide 66: Gradient of a Scalar Field (example)
Magnitude  Rate of maximum increase
Direction  Steepest ascent
f(x = 9, y = 2, z = 3) = 6
P: (x = 9, y = 2, z = 3)
P
l
f = 6
l = 0.1
f = 5.9
f = 5.8
f = 5.9
f = 6
f = 6.1
f = 6.2
f = 6.1
Gradient direction

## Slide 67: Gradient and Equipotential Surfaces
A scalar field f(x, y, z) assigns a number to every point in space.
A level surface (or equipotential surface) is the locus of all points satisfying:
f(x, y, z) = constant
At any point P, the gradient vector of a scalar field is perpendicular (normal) to the equipotential surface that passes through P.
f = 1.5
f = 1.6
f = 1.4
P: (x0, y0, z0)
f
f = f(x0, y0, z0)

## Slide 68: Directional Derivative
Directional derivative is the rate at which a scalar field f changes at a point P in a specific direction ( ).
P
f
O
Directional derivative

## Slide 69: Fundamental Theorem for Gradient
The line integral of a gradient field depends only on the endpoints (P1 and P2), not on the path taken (C).
C
P1
P2

## Slide 70: Fundamental Theorem for Gradient (cont.)
O

## Slide 71: Gradient in Orthogonal Curvilinear Coordinates
General orthogonal curvilinear coordinate system (u1​,u2​,u3​) with metric coefficients h1, h2, h3

## Slide 72: Gradient in Cartesian Coordinates
u1​ = x, u2​ = y, u3​ = z
h1 = 1, h2 = 1 , h3 = 1

## Slide 73: Gradient in Cylindrical Coordinates
u1​ = r, u2​ = , u3​ = z
h1 = 1, h2 = r , h3 = 1

## Slide 74: Gradient in Spherical Coordinates
u1​ = R, u2​ = , u3​ = 
h1 = 1, h2 = R, h3 = R sin

## Slide 75: Gradient of a Scalar Field (example)
f1 = x
f2 = r cos
f 3 = R sin cos

## Slide 76: Divergence of a Vector Field
Input: a vector field, e.g. F(R) Output: a scalar field, e.g. f(R)
Vector field
Scalar field
Divergence symbol

## Slide 77: Flux of a Vector Field
Flux is the net flow of a vector field F passing through a surface S along its normal direction.
Vector field (F): red arrows
Unit normal vector ( ): blue arrows

## Slide 78: Definition of Divergence
Divergence is the flux of a vector field per unit volume, as the volume shrinks to a point.
S: the closed surface bounding the volume Δv.
Flux out of Δv

## Slide 79: Divergence of a Vector Field (example)
F
F
F

## Slide 80: Fundamental Theorem for Divergence
V
S
Divergence theorem

## Slide 81: Fundamental Theorem for Divergence (cont.)
V
S
v

## Slide 82: Divergence in Orthogonal Curvilinear Coordinates
General orthogonal curvilinear coordinate system (u1​,u2​,u3​) with metric coefficients h1, h2, h3

## Slide 83: Divergence in Cartesian Coordinates
u1​ = x, u2​ = y, u3​ = z
h1 = 1, h2 = 1 , h3 = 1

## Slide 84: Divergence in Cylindrical Coordinates
u1​ = r, u2​ = , u3​ = z
h1 = 1, h2 = r , h3 = 1

## Slide 85: Divergence in Spherical Coordinates
u1​ = R, u2​ = , u3​ = 
h1 = 1, h2 = R, h3 = R sin

## Slide 86: Divergence of a Vector Field (example)

## Slide 87: Curl of a Vector Field
Input: a vector field, e.g. G(R) Output: a vector field, e.g. F(R)
Vector field
Vector field
Curl symbol

## Slide 88: Circulation of a Vector Field
Circulation (or rotation) of a vector field F around a closed path C is defined as the scalar line integral of the vector over the path.
C

## Slide 89: Definition of Curl
The curl of a vector field F is a vector
  whose magnitude is the net circulation of F per unit area as the area tends to zero, and
  whose direction is the normal direction of the area when the area is oriented to make the net circulation maximum (right-hand rule).
C
s

## Slide 90: Fundamental Theorem for Curl
C
S
ds
Stokes’ theorem

## Slide 91: Fundamental Theorem for Curl (cont.)
C
S
C1
C2

## Slide 92: Volume Integral of the Curl of a Vector Field
It shows that the net curl content inside a volume manifests as a tangential surface effect.
V
S

## Slide 93: Volume Integral of the Curl of a Vector Field
Let C be any constant vector.
V
S

## Slide 94: Curl in Orthogonal Curvilinear Coordinates
General orthogonal curvilinear coordinate system (u1​,u2​,u3​) with metric coefficients h1, h2, h3

## Slide 95: Curl in Cartesian Coordinates
u1​ = x, u2​ = y, u3​ = z
h1 = 1, h2 = 1 , h3 = 1

## Slide 96: Curl in Cylindrical Coordinates
u1​ = r, u2​ = , u3​ = z
h1 = 1, h2 = r , h3 = 1

## Slide 97: Curl in Spherical Coordinates
u1​ = R, u2​ = , u3​ = 
h1 = 1, h2 = R, h3 = R sin

## Slide 98: Curl of a Vector Field (example)

## Slide 99: Two Null Identities

## Slide 100: Irrotational and Solenoidal Fields
A vector field F is solenoidal (or divergenceless) if its divergence is zero at every point.
A vector field F is irrotational (or conservative) if its curl is zero at every point.

## Slide 101: Features of Solenoidal Fields
Source free
1)
2)

## Slide 102: Features of Irrotational Fields
Path independent
1)
2)

## Slide 103: Classification of Vector Fields
Solenoidal and irrotational
Solenoidal but not irrotational
Irrotational but not solenoidal
Neither solenoidal nor irrotational

## Slide 104: Helmholtz’s Theorem
A vector field is determined to within an additive constant if both its divergence and its curl are specified everywhere.

## Slide 105: Helmholtz’s Theorem (cont.)
A general vector field F can be written as